## Slide 1
Chapter 1 Computer Networks and the Internet
A note:
Most parts of these ppt slides are borrowed from the slides for “A Top Down Approach Featuring the Internet, 2nd edition” authored by “Jim Kurose and Keith Ross.

## Slide 2: Chapter 1: Introduction
Our goal:
get context, overview, “feel” of networking
more depth, detail later in course
approach:
  descriptive
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
Internet/ISP structure
performance: loss, delay
protocol layers, service models
history

## Slide 3: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 4: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts, end-systems
  PCs workstations, servers
  PDAs phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)
local ISP
company
network
regional ISP
router
workstation
server
mobile
IDC

## Slide 5: What’s a protocol?
network protocols:
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 6: What’s a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
req
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 7: A closer look at network structure:
network edge: applications and hosts
  PC, Server, Notebook, PDA, Cellular phone, …
Notes: 여기 등장하는 그림을 기본으로 사용하는 것이 좋겠다.
그러나, 일부 수정하는 것이 좋겠다.
핸드폰 등 이동통신망 관련 추가,
가정 자동화 관련 추가,
HFC 관련 그림 추가
이 그림을 기본으로 여러 용도로 사용할 필요가 있다.
예를 들면, 용어 설명(네트워크 에지, 네트워크 코어, access network, …) , 혼잡 발생 시나리오,
뜨거우니까 문제지.

## Slide 8: A closer look at network structure:
network core:
  routers
    Edge router vs core router
    Backbone router
  network of networks
Notes: 여기 등장하는 그림을 기본으로 사용하는 것이 좋겠다.
그러나, 일부 수정하는 것이 좋겠다.
핸드폰 등 이동통신망 관련 추가,
가정 자동화 관련 추가,
HFC 관련 그림 추가
이 그림을 기본으로 여러 용도로 사용할 필요가 있다.
예를 들면, 용어 설명(네트워크 에지, 네트워크 코어, access network, …) , 혼잡 발생 시나리오,
뜨거우니까 문제지.

## Slide 9: A closer look at network structure:
access networks, physical media
  communication links
    Copper, telephone, wireless (IEEE 802.11b, CDMA), …
  over 80% of the total network size

## Slide 10: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 11: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Gnutella, KaZaA

## Slide 12: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 13: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 14: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 15: Access networks and physical media
Q: How to connection end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 16: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (often less)
  Can’t surf and phone at same time: can’t be “always on”
ADSL: asymmetric digital subscriber line
  up to 1 Mbps upstream (today typically < 256 kbps)
  up to 8 Mbps downstream (today typically < 1 Mbps)
  FDM: 50 kHz - 1 MHz for downstream
  4 kHz - 50 kHz for upstream
  0 kHz - 4 kHz for ordinary telephone

## Slide 17: Residential access: cable modems
HFC: hybrid fiber coax
  asymmetric: up to 10Mbps upstream, 1 Mbps downstream
network of cable and fiber attaches homes to ISP router
  shared access to router among home
  issues: congestion, dimensioning
deployment: available via cable companies, e.g., MediaOne

## Slide 18: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 19: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 20: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 21: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM:

## Slide 22: Company access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated link connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs happening now
LANs: chapter 5

## Slide 23: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b (WiFi): 11 Mbps
wider-area wireless access
  provided by telco operator
  3G ~ 384 kbps
    Will it happen??
  WAP/GPRS in Europe
base
station
mobile
hosts
router

## Slide 24: Home networks
Typical home network components:
ADSL or cable modem
router/firewall/NAT
Ethernet
wireless access
point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet
(switched)

## Slide 25: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5 TP: 100Mbps Ethernet

## Slide 26: Physical Media: coax, fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channel on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 5 Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 27: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WaveLAN)
  2Mbps, 11Mbps
wide-area (e.g., cellular)
  e.g. 3G: hundreds of kbps
satellite
  up to 50Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus LEOS

## Slide 28: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 29: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 30: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 31: Internet protocol stack
application: supporting network applications
  FTP, SMTP, STTP
transport: host-host data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 32: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 33: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 34: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 35: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 36: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 ISPs and Internet backbones
  1.6 Delay & loss in packet-switched networks
  1.7 Internet structure and ISPs
  1.8 History

## Slide 37: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 38: Internet History
1970: ALOHAnet satellite network in Hawaii
1973: Metcalfe’s PhD thesis proposes Ethernet
1974: Cerf and Kahn - architecture for interconnecting networks
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 39: Internet History
1983: deployment of TCP/IP
1982: SMTP e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: FTP protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 40: Internet History
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
Late 1990’s – 2000’s:
more killer apps: instant messaging, peer2peer file sharing (e.g., Naptser)
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps

## Slide 41: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
Internet/ISP structure
performance: loss, delay
layering and service models
history
You now have:
context, overview, “feel” of networking
more depth, detail to follow!