## Slide 1
Chapter 20
Network Layer Protocols:
ARP, IPv4, ICMPv4, IPv6, and ICMPv6

## Slide 2
Figure 20.1 Protocols at network layer

## Slide 3
20.1 ARP
Mapping
Packet Format
Encapsulation
Operation

## Slide 4
Figure 20.2 ARP operation

## Slide 5
Figure 20.4 Encapsulation of ARP packet

## Slide 6
An ARP request is broadcast; an ARP reply is unicast.
Note:

## Slide 7
20.2 IP
Datagram
Fragmentation

## Slide 8
Figure 20.7 IP datagram
Higher-level protocol that uses the services of the IP layer
e.g., TCP, UDP, ICMP, …
Fragmentation
related fields

## Slide 9
The total length field defines the total length of the datagram including the header.
Note:

## Slide 10
Figure 20.8 Multiplexing

## Slide 11
Figure 20.9 Example of checksum calculation

## Slide 12: Fragmentation
Why do we need fragmentation of IP packet?
PC
R
R
R
PC
MTU=1500
MTU=500
MTU=1000
MTU=1500

## Slide 13
Figure 20.10 MTU

## Slide 14: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 15: IP Fragmentation and Reassembly
ID
=x
offset
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1400
ID
=x
offset
=175
fragflag
=1
length
=1400
ID
=x
offset
=350
fragflag
=0
length
=1200
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1400 bytes
3 bits
13 bits
Reserved
Frag./no frag.
More fragment bit
Offset*8=byte offset
0000 0101 0111 1000
0000 0101 0111 1
1400
175

## Slide 16
20.3 ICMP
Types of Messages

## Slide 17: ICMP
Why ICMP?
  IP has no error-reporting or error-correcting mechanism. What happens if something goes wrong?
    E.g., a router cannot find a router to the final destination, given a packet
  IP lacks a mechanism for host and management queries
    E.g., Is a router alive?

## Slide 18
Figure 20.12 ICMP encapsulation

## Slide 19
ICMP always reports error messages to the original source.
Note:

## Slide 20: Error-reporting messages of ICMP (1)
Destination unreachable
  When a router cannot route a datagram or a host cannot deliver a datagram
    The datagram is discarded, and the router or the host sends a destination unreachable message back to the source host
Source quench
  Since IP does not perform flow control and congestion control, the source host never knows if the destination host has been overwhelmed with datagrams
    When a router or host discards a datagram due to congestion, it sends a source-quench message to the sender
Time exceeded
  A time-exceeded message is sent to the source when
    A router receives a packet with 0-valued TTL
    All fragments do not arrived at a certain time limit at the destination host

## Slide 21: Error-reporting messages of ICMP (2)
Parameter problem
  A parameter-problem ICMP packet is sent to the source if
    A router or the destination host discovers an ambiguous or missing value in any field of the datagram
Redirection
  Since a host usually use static routing, the host may send a packet to the default router which may be a wrong router. In this case, if the default router knows the correct router, it sends a redirection message back to the host.

## Slide 22
Figure 20.13 Error-reporting messages

## Slide 23
There is no flow control or congestion control mechanism in IP.
Note:

## Slide 24: Query in ICMP
Echo request and replay
  i.e., ping ei.chonbuk.ac.kr
Time-stamp request and replay
  To determine the round-trip time
Address mask request and reply
  Given a address mask request message to a router, the router sends a mask in an address mask reply message
Router solicitation and advertisement
  Why?
    A host needs to know the address of routers connected to its own network to send data to a host on another network
  Given a router solicitation message from a host, router(s) broadcast their routing information using the router-advertisement message

## Slide 25
20.4 IPv6
IPv6 Addresses
Categories of Addresses
IPv6 Packet Format
Fragmentation
ICMPv6
Transition

## Slide 26: IPv6 (IPng)
Advantages over IPv4
  Larger address space
    128 bits
  Better header format
    This simplifies and speeds up the routing process since most of the options are not need to be checked by routers
  New options
  Allowance for extension
  Support for research allocation
    Flow label instead of type-of-service field
  Support for more security

## Slide 27
Figure 20.15 IPv6 address
Hexadecimal colon notation

## Slide 28
Figure 20.16 Abbreviated address

## Slide 29
Figure 20.17 Abbreviated address with consecutive zeros

## Slide 30
Figure 20.19 Format of an IPv6 datagram

## Slide 31
Figure 20.20 Comparison of network layers in version 4 and version 6

## Slide 32
Figure 20.21 Three transition strategies

## Slide 33
Figure 20.22 Dual stack
What problems?
IPv4
IPv4
IPv6
IPv6
IPv4-IPv6
X

## Slide 34
Figure 20.23 Tunneling
IPv6
IPv6
IPv4
IPv4
IPv4
IPv4
IPv4/IPv6
IPv4/IPv6

## Slide 35
Figure 20.24 Header translation
IPv6
IPv4
IPv4-IPv6 Very limited!
IPv6 flow label problem

## Slide 36: Fundamental problems for IPv6 translation
Router replacement!