## Slide 1
Chapter 23
Congestion Control and Quality of Service

## Slide 2
23.1 Data Traffic
Traffic Descriptor
Traffic Profiles

## Slide 3: 데이터 트래픽
왜 갑자기 데이터 트래픽 이야기?
  네트워크 혼잡(congestion)과 품질(QoS)은 결국 사용자로부터 들어오는 데이터 트래픽 양을 조절하거나 서비스 양을 달리하는 것
  양을 조절하려면 얼마나 어떤 식으로 들어오는 지 정량화 해야 함
  가장 간단한 정량화 방법: 평균!
    Average data rate = amount of data / time
    문제점
      평균은 단위 시간에 들어오는 양이 일정할 때 유용하지만 실제 인터넷 트래픽은 그렇지 않음
      이해가 잘 안된다고? -> 다음 페이지

## Slide 4: 평균의 함정!
100
200
50
200
시간
양
10
20
50
200
(100+200+50+20)/200
양
10
20
1.6
1.3
2.75
위의 트래픽을 시간에 따른 평균양으로 나타내면 어떤것?
단위 시간

## Slide 5: 데이터 트래픽 기술 방법
평균의 경우
  기준이 되는 시간은 “경우에 따라 알맞게”
    예1: 과금이 목적이면 시간은 1달
    예2: TCP 성능 측정이 목적이면 시간은 RTT 시간
데이터 트래픽을 기술하는 일반적인 방법
  시간 구간에 대해 최대량을 기술
  Amount = f(t)
    함수 f는 non-decreasing function
시간 구간
양
기울기가 감소하지 않음(같거나 큼)

## Slide 6: 데이터 트래픽 기술 방법
트래픽을 라우터가 쉽게 측정하기 위해서는 간단한 non-decreasing 함수만 사용
  가장 널리 쓰이는 형태
    Amount = max( line A, line B)
시간 구간
양
Burstyness
Peak rate
Average rate
Line A
Line B

## Slide 7
Figure 23.1 Traffic descriptors

## Slide 8
Figure 23.2 Constant-bit-rate traffic

## Slide 9
Figure 23.3 Variable-bit-rate traffic

## Slide 10
Figure 23.4 Bursty traffic

## Slide 11
23.2 Congestion
Network Performance

## Slide 12: 혼잡(congestion)
혼잡은 네트워크에 걸리는 로드가 네트워크 용량을 초과하면 발생할 수 있음
혼잡 제어(congestion control)은 네트워크 용량이 초과될 때 네트워크 처리 용량 한계 이하로 낮추는 메커니즘
혼잡이 발생하는 이유?
  고속도로에 너무 많은 차가 진입하면 교통체증을 앓는 것과 같은 이유
라우터 버퍼는 일시적인 혼잡을 해결하기 위한 것
  전체적인 입력 데이터 양이 네트워크 처리 용량을 초과하지 않지만 순간적으로 많은 양이 들어오는 것을 처리
  따라서 라우터 버퍼는 일시적인 bursty 데이터를 저장할 크기 정도가 적당함

## Slide 13
Figure 23.5 Incoming packet

## Slide 14
Figure 23.6 Packet delay and network load

## Slide 15
Figure 23.7 Throughput versus network load

## Slide 16
23.3 Congestion Control
Open Loop
Open Loop
Closed Loop

## Slide 17
23.4 Two Examples
Congestion Control in TCP
Congestion Control in Frame Relay

## Slide 18: TCP Congestion Control
end-end control (no network assistance)
sender limits transmission:
LastByteSent-LastByteAcked
 CongWin
Roughly,
CongWin is dynamic, function of perceived network congestion
How does sender perceive congestion?
loss event = timeout or 3 duplicate acks
TCP sender reduces rate (CongWin) after loss event
three mechanisms:
  AIMD
  slow start
  conservative after timeout events
rate =
CongWin
RTT
Bytes/sec

## Slide 19: TCP AIMD
multiplicative decrease: cut CongWin in half after loss event
additive increase: increase CongWin by 1 MSS every RTT in the absence of loss events: probing
Long-lived TCP connection
왜 절반을 줄일까?

## Slide 20: TCP Slow Start
When connection begins, CongWin = 1 MSS
  Example: MSS = 500 bytes & RTT = 200 msec
  initial rate = 20 kbps
available bandwidth may be >> MSS/RTT
  desirable to quickly ramp up to respectable rate
When connection begins, increase rate exponentially fast until first loss event

## Slide 21: TCP Slow Start (more)
When connection begins, increase rate exponentially until first loss event:
  double CongWin every RTT
  done by incrementing CongWin for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 22: Refinement
After 3 dup ACKs:
  CongWin is cut in half
  window then grows linearly
But after timeout event:
  CongWin instead set to 1 MSS;
  window then grows exponentially
  to a threshold, then grows linearly
3 dup ACKs indicates network capable of delivering some segments
timeout before 3 dup ACKs is “more alarming”
Philosophy:

## Slide 23: Refinement (more)
Q: When should the exponential increase switch to linear?
A: When CongWin gets to 1/2 of its value before timeout.
Implementation:
Variable Threshold
At loss event, Threshold is set to 1/2 of CongWin just before loss event

## Slide 24: Summary: TCP Congestion Control
When CongWin is below Threshold, sender in slow-start phase, window grows exponentially.
When CongWin is above Threshold, sender is in congestion-avoidance phase, window grows linearly.
When a triple duplicate ACK occurs, Threshold set to CongWin/2 and CongWin set to Threshold.
When timeout occurs, Threshold set to CongWin/2 and CongWin is set to 1 MSS.

## Slide 25
TCP assumes that the cause of a lost segment is due to congestion in the network.
Note:

## Slide 26
If the cause of the lost segment is congestion, retransmission of the segment does not remove the cause—it aggravates it.
Note:

## Slide 27
Figure 23.8 Multiplicative decrease
Slow start
Additive increase

## Slide 28: 무선환경에서의 TCP 혼잡제어의 문제점
유선환경에서는 TCP가 거의 완벽하게 동작
문제는 무선(wireless) 환경(WiFi, 4G, 5G, …)!
왜?
  무선환경은 패킷 전송 오류가 빈번하게 일어남
  TCP sender는 단순한 패킷 전송 오류를 “혼잡으로 착각“
    쓸데없이 전송율을 절반으로 줄임
    예: 무선랜 12 Mbps에서 혼자 사용해도 5 Mbps 밖에 나오지 않는 경우
대응방법
  무선환경에 적응하는 “Wireless” TCP 프로토콜 개발
    호환성의 문제점!
  무선환경 자체에 패킷 전송 오류를 보완하는 방법(next slide)

## Slide 29
단말
기지국
PHY
LINK
IP
TCP
PHY
LINK
GW
Internet
Frame with FEC
Frame
Tx. schedule
Retransmit Req.
Frame
Case 1
Case 2
…
핵심은 패킷 오류를 잘 발생하지 않게!